## Slide 1: Applied Physics 204 Course Project DeVry University Professor- Susan Tabbaa Nachawati, Ph.D
Ashley Kennedy
April/2022

## Slide 2: Introduction
Materials used
Precision of ultrasonic sensor
Gravitational acceleration of free falling objects
Conservation of energy from free falling objects
Rotational Motion
Hall Effect

## Slide 3: PHYS204 Project Part 1
Materials List

## Slide 4: Materials List (Picture)
Mega 2560 Board
Ultrasonic sensor HC-SR04
Male to Male Wires
Breadboard
USB cable
Ruler or tape measurer
Object to act as obstacle and/or undergo free-fall

## Slide 5: Materials List (Picture)
Mega 2560 Board
Rotary Encoder Part KY-040
Male to Female Wires
USB cable
Object to attach onto rotary encoder
Ruler or tape measurer

## Slide 6: Materials List (Picture)
ESP32 microprocessor
Micro-USB to USB cable
Magnet

## Slide 7: Required Software (screenshot)
Microsoft Excel installed and running on your computer

## Slide 8: Required Software (screenshot)
Arduino IDE installed and running on your computer

## Slide 9: PHYS204 Project Part 2
Precision of the Ultrasonic Sensor

## Slide 10: Experimental Set-up (Picture)
Materials List:
Mega 2560 Board
Ultrasonic sensor HC-SR04
Male to Male Wires
Breadboard
Ruler or tape measurer
Object to act as obstacle

## Slide 11: Raw Data (Screenshot)
Screenshot of Serial Monitor from Arduino IDE showing raw data.
Must include your name displayed in the serial monitor.
Make sure “show timestamp” is NOT selected.

## Slide 12: Data Collection
Trial | Ruler Distance (cm) | Total Roundtrip Distance (m) | Time from Serial Monitor (microseconds) | Roundtrip time (s) | Velocity = distance/time (m/s)
1 | 2.54 | .05 | 270 | 2.70e-4 | 185
2 | 5.08 | .10 | 347 | 3.47e-4 | 288
3 | 7.62 | .15 | 566 | 5.66e-4 | 265
4 | 10.16 | .20 | 785 | 7.85e-4 | 254
5 | 15.24 | .30 | 1000 | 10.00e-4 | 300

## Slide 13: Data Analysis
Average velocity from table
Percent difference where
m/s
m/s
25%
258

## Slide 14: Conclusions
Discuss the results and comment on the source of errors.
  Answer: I had the percentage because I didn’t multiply the distance by 2 for the round trip. I ran into issues with the percent difference and re-ran the numbers multiple times. I still don’t feel 100% right about the 25% difference and I’m confused how the Velocity can fluctuate down at greater distances and speeds and then also go back up.
What is the dependence of temperature, humidity, and atmospheric pressure on the speed of sound? How does it affect the results?
  Answer: Pressure and humidity don’t have a huge effect on speed of sound. Heat is a form of kinetic energy just like sound thus it causes sound to travel faster.

## Slide 15: PHYS204 Project Part 3
Gravitational Acceleration of Free Falling Object

## Slide 16: Experimental Set-up (Picture)
Materials List:
Mega 2560 Board
Ultrasonic sensor HC-SR04
Male to Male Wires
Breadboard
Object to undergo free fall motion

## Slide 17: Serial Monitor (Screenshot)
Include screenshot of raw data showing the start of the fall and end of the fall of one trial.
Must include your name displayed in the serial monitor.
Make sure “show timestamp” is NOT selected.

## Slide 18: Excel Table (Screenshot)
Include all values in the Excel table for a single trial showing the fall distance in centimeters and meters as a function of time

## Slide 19: Excel Graph (Screenshot)
Include Excel graph for a single trial showing the fall distance as a function of time.
Must include equation for curve fitting.

## Slide 20: Data Collection
Trial | x2 coefficient value from curve fitting | Acceleration (m/s2) = 2* (x2 coefficient)
1 | 5.50 | 11 m/s2
2 | 3.98 | 7.96 m/s2
3 | 3.40 | 6.80 m/s2
4 | 4.51 | 9.02 m/s2
5 | 3.34 | 6.68 m/s2

## Slide 21: Data Analysis
Average acceleration from table
Percent difference with
m/s2
15.4%
m/s2
8.29

## Slide 22: Conclusions
Discuss the results and comment on the source of errors.
  Answer: Didn’t really have any errors. Hardest part was the trials and getting a clear reading.
How much variation is there from trial to trial? What does this indicate about the uncertainty of the result?
  Answer: Wide range of variation at about 15.4% Such variations could deem tests and trials unreliable as its quite the deviation.

## Slide 23: PHYS204 Project Part 4
Conservation of Energy of Free Falling Object

## Slide 24: Excel Table (Screenshot)
Include all values in the Excel table for a single trial showing the fall distance in centimeters and meters as a function of time with the values generated for kinetic energy K, potential energy U, and total mechanical energy E.

## Slide 25: Excel Graph (Screenshot)
Include Excel graph for a single trial showing the plots of the kinetic energy K, potential energy U, and total mechanical energy E as a function of time.
Must include your name in the title of the graph.

## Slide 26: Data Validation
Theoretical value of final velocity
Final velocity from experimental data (or largest velocity)
Percent difference
=
0.55
m/s
9.8%
0.61
m/s
0.0188
m

## Slide 27: Conclusions
Discuss the key characteristics of the plot. Consider the times when potential energy U is max, U is min, kinetic energy K is max, K is min, and when U and K are the same value. What is the significance of these points?
  Answer: Potential energy is at its max at the beginning and Kinetic anergy rises and reaches its max at value at the end of the trial.

## Slide 28: Conclusions
What is the trend of the best fit line for the total energy E in your data? If the data is accurate, the total mechanical energy should decrease slightly. Why is that?
  Answer: I believe the total mechanical energy decreases due to forces of gravity and outside forces such as air.

## Slide 29: PHYS204 Project Part 5
Rotational Motion

## Slide 30: Experimental Set-up (Picture)
Materials List:
Mega 2560 Board
Rotary Encoder Part KY-040
Male to Female Wires
Object to attach onto rotary encoder (e.g. cork, bottle cap, ball)
Ruler or tape measurer

## Slide 31: Raw Data (Screenshot)
Screenshot of Serial Monitor from Arduino IDE showing raw data.
Must include your name displayed in the serial monitor.

## Slide 32: Data Collection
Object diameter: d =
Object radius: r =
Number of pulses for one revolution: x =
Resolution =
3.9
cm
1.95
cm
0.209
Radians/pulse
30

## Slide 33: Data Analysis
Trial | Number of pulses N | Encoder distance r N | Measured distance with ruler | Percent difference
1 | 26 | 1.95*.209*26=10.6cm | 10cm | 30-10.6/10=1.94*100 =194%
2 | 49 | 1.95*.209*20=20.0cm | 20cm | 30-20.0/20=.5*100 =50%
3 | 63 | 1.95*.209*63=25.7cm | 26cm | 30-25.7/26=.17*100 =17%
4 | 70 | 1.95*.209*70=28.5cm | 30cm | 30-28.5/30=.05*100 =5%
5 | 130 | 1.95*.209.130=53.0cm | 55cm | 30-53.0/55=.41*100 =41%
Trial | Number of pulses N |  | Measured distance with ruler | Percent difference
1 | 26 | 1.95*.209*26=10.6cm | 10cm | 30-10.6/10=1.94*100 =194%
2 | 49 | 1.95*.209*20=20.0cm | 20cm | 30-20.0/20=.5*100 =50%
3 | 63 | 1.95*.209*63=25.7cm | 26cm | 30-25.7/26=.17*100 =17%
4 | 70 | 1.95*.209*70=28.5cm | 30cm | 30-28.5/30=.05*100 =5%
5 | 130 | 1.95*.209.130=53.0cm | 55cm | 30-53.0/55=.41*100 =41%

## Slide 34: Conclusions
Discuss the results and comment on the sources of error.
  Answer: The % differences seem to have dramatic differences within the experiment noted in the table of the previous slide.
  The rotary sensor slides and it could take several tries to get an accurate reading.
What are some applications of this measuring technique? Could this measuring system be used to measure surfaces that are not flat?
  Answer: I find that this measuring technique isn’t great for measuring even flat surfaces as the size and texture of the object used makes a huge difference in the rotary sensor being reliable and getting functional results. I don’t believe this specific technique with these tools would be any better for non flat surfaces.

## Slide 35: PHYS204 Project Part 6
Hall Effect

## Slide 36: Experimental Set-up (Picture)
Materials List:
ESP32 microprocessor
Micro-USB cable
Magnet

## Slide 37: Raw Data (Screenshot)
Screenshot of Serial Monitor from Arduino IDE showing raw data.
Must include your name displayed in the Serial Monitor.
Press EN button to display name.
Unselect “Autoscroll” and scroll all the way up.

## Slide 38: Data Analysis (Screenshot)
Screenshot data plotted in Excel.

## Slide 39: Conclusions
Discuss the results and comment on the sources of error.
  Answer: I didn’t have access to a magnet with a stronger force and at times even flipping the magnet didn’t give me an opposite reaction in the serial monitor.
Describe how the Hall sensor works. What are some applications for the Hall effect sensor?
  Answer:” ESP32 microprocessor to measure the proportional voltage under the effect of a magnetic field. The hall effect sensor is located behind the metal lid of the ESP32 chip. The measurements from the sensor can increase or become negative depending on the magnet pole facing the sensor.”-course module Template

## Slide 40: Challenges Throughout Project
Percent difference was confusing and hard to convert for me due to large discrepancies in the sensors.
Sensors were unstable causing larger fluctuation in the data
Getting clear readings with sensors and having to do multiple trial runs to get clean figures for the data analysis
Rotary sensor was difficult to use finding the perfect object to attach and a surface with enough traction was a huge challenge in getting that sensor to work properly for testing.

## Slide 41: Career skills Obtained from Project
Patience
Broader understanding of Applied Physics
Experience with Sensors wiring and coding
Creating spreadsheets and graphs in Excel
Producing and crafting Power Points
Following instructions
Recording Data

## Slide 42: The End